## Slide 1: William Stallings Data and Computer Communications
Chapter 4
Transmission Media

## Slide 2: Overview
Guided - wire
Unguided - wireless
Characteristics and quality determined by medium and signal
For guided, the medium is more important
For unguided, the bandwidth produced by the antenna is more important
Key concerns are data rate and distance

## Slide 3: Design Factors
Bandwidth
  Higher bandwidth gives higher data rate
Transmission impairments
  Attenuation
Interference
Number of receivers
  In guided media
  More receivers (multi-point) introduce more attenuation

## Slide 4: Electromagnetic Spectrum

## Slide 5: Guided Transmission Media
Twisted Pair
Coaxial cable
Optical fiber

## Slide 6: Twisted Pair

## Slide 7: Twisted Pair - Applications
Most common medium
Telephone network
  Between house and local exchange (subscriber loop)
Within buildings
  To private branch exchange (PBX)
For local area networks (LAN)
  10Mbps or 100Mbps

## Slide 8: Twisted Pair - Pros and Cons
Cheap
Easy to work with
Low data rate
Short range

## Slide 9: Twisted Pair - Transmission Characteristics
Analog
  Amplifiers every 5km to 6km
Digital
  Use either analog or digital signals
  repeater every 2km or 3km
Limited distance
Limited bandwidth (1MHz)
Limited data rate (100MHz)
Susceptible to interference and noise

## Slide 10: Unshielded and Shielded TP
Unshielded Twisted Pair (UTP)
  Ordinary telephone wire
  Cheapest
  Easiest to install
  Suffers from external EM interference
Shielded Twisted Pair (STP)
  Metal braid or sheathing that reduces interference
  More expensive
  Harder to handle (thick, heavy)

## Slide 11: UTP Categories
Cat 3
  up to 16MHz
  Voice grade found in most offices
  Twist length of 7.5 cm to 10 cm
Cat 4
  up to 20 MHz
Cat 5
  up to 100MHz
  Commonly pre-installed in new office buildings
  Twist length 0.6 cm to 0.85 cm

## Slide 12: Near End Crosstalk
Coupling of signal from one pair to another
Coupling takes place when transmit signal entering the link couples back to receiving pair
i.e. near transmitted signal is picked up by near receiving pair

## Slide 13: Coaxial Cable

## Slide 14: Coaxial Cable Applications
Most versatile medium
Television distribution
  Ariel to TV
  Cable TV
Long distance telephone transmission
  Can carry 10,000 voice calls simultaneously
  Being replaced by fiber optic
Short distance computer systems links
Local area networks

## Slide 15: Coaxial Cable - Transmission Characteristics
Analog
  Amplifiers every few km
  Closer if higher frequency
  Up to 500MHz
Digital
  Repeater every 1km
  Closer for higher data rates

## Slide 16: Optical Fiber

## Slide 17: Optical Fiber - Benefits
Greater capacity
  Data rates of hundreds of Gbps
Smaller size & weight
Lower attenuation
Electromagnetic isolation
Greater repeater spacing
  10s of km at least

## Slide 18: Optical Fiber - Applications
Long-haul trunks
Metropolitan trunks
Rural exchange trunks
Subscriber loops
LANs

## Slide 19: Optical Fiber - Transmission Characteristics
Act as wave guide for 1014 to 1015 Hz
  Portions of infrared and visible spectrum
Light Emitting Diode (LED)
  Cheaper
  Wider operating temp range
  Last longer
Injection Laser Diode (ILD)
  More efficient
  Greater data rate
Wavelength Division Multiplexing

## Slide 20: Optical Fiber Transmission Modes

## Slide 21: Wireless Transmission
Unguided media
Transmission and reception via antenna
Directional
  Focused beam
  Careful alignment required
Omnidirectional
  Signal spreads in all directions
  Can be received by many antennae

## Slide 22: Frequencies
2GHz to 40GHz
  Microwave
  Highly directional
  Point to point
  Satellite
30MHz to 1GHz
  Omnidirectional
  Broadcast radio
3 x 1011 to 2 x 1014
  Infrared
  Local

## Slide 23: Terrestrial Microwave
Parabolic dish
Focused beam
Line of sight
Long haul telecommunications
Higher frequencies give higher data rates

## Slide 24: Satellite Microwave
Satellite is relay station
Satellite receives on one frequency, amplifies or repeats signal and transmits on another frequency
Requires geo-stationary orbit
  Height of 35,784km
Television
Long distance telephone
Private business networks

## Slide 25: Broadcast Radio
Omnidirectional
FM radio
UHF and VHF television
Line of sight
Suffers from multipath interference
  Reflections

## Slide 26: Infrared
Modulate noncoherent infrared light
Line of sight (or reflection)
Blocked by walls
e.g. TV remote control, IRD port

## Slide 27: Required Reading
Stallings Chapter 4